## Slide 1
Ministry of the Environment
Land and Sea
DETERMINING THE FUTURE OF FLOOD-RELATED RESEARCH IN EUROPE
WORKSHOP ON CRUE’S RESEARCH AGENDA
Budapest, 23rd April 2008
FLOOD RISK MANAGEMENT IN ITALY:
TOOLS FOR HYDROGEOLOGICAL LAND PLANNING
Maria Grazia Cotta
Ministry of the Environment Land and Sea
Directorate for Soil Protection
Directorate for Soil Protection

## Slide 2
Ministry of the Environment
Land and Sea
Water is a vital element and a precious resource,
but, at times, a danger to be controlled and above all avoided.
Directorate for Soil Protection

## Slide 3
Ministry of the Environment
Land and Sea
Directorate for Soil Protection
Polesine 1951
Florence 1966
Genoa 1970
Sarno 1998
Piedmont 2000
Piedmont 2000
Floods are natural phenomena which periodically affect every part of the planet.
Italy has a very long history of disasters caused by floods (Polesine 1951, Florence 1966, Genoa 1970, Versilia 1996, Sarno 1998, Piedmont 1994 e 2000) that invariably affected plains sweeping away houses and farmlands, damaging all properties and causing loss of human lives.
Faced with certain events of great dimensions and high energies man often cannot resist.
The natural phenomena and the hydrogeological instabilities

## Slide 4
Ministry of the Environment
Land and Sea
Directorate for Soil Protection
Polesine 1951
Florence 1966
Genoa 1970
Sarno 1998
Piedmont 2000
Piedmont 2000
Saving human health and live and protection of properties and the environment from flooding events can be achieved through:
  knowledge of phenomena,
  land surveying and simulations of potential floods,
  impact assessment on the built up areas and the consequent risk and
  adoption of defence measures, where considered worthwhile to avoid further calamities .
The concepts of prevention and protection

## Slide 5
Piedmont 1994
Versilia 1996
Friuli 2003
Apulia 2005
Ministry of the Environment
Land and Sea
Directorate for Soil Protection
The prevention and protection concepts have been implemented by establishing rules responding to the appropriate land management principles.
The river basin has been identified as basic unit for developing adequate land management in an integrated, multisectorial way and through consultation.
On this basis, in 1989, the first Law for the “soil protection” in Italy was enacted; the Law set the rules for actions needed to ensure the hydrogeological land planning, for the safety of population, the protection of properties cultural heritage, the environment and human activities.
The principles and the rules

## Slide 6
Piedmont 1994
Versilia 1996
Friuli 2003
Apulia 2005
Ministry of the Environment
Land and Sea
Directorate for Soil Protection
Later, in 1998, in order to strengthen and enhance the previous Law, a new Act entered into force, defining criteria and procedures to obtain hydrogeological land planning aimed at more clearly applying the concept of protection.
The concept of risk was introduced, as a result of the combination of hazard, value and vulnerability of the elements at risk.
Limitation of land use was defined, aimed at avoiding new risk , and also measures to reduce the existing risk through its classification, identifying the degree of attention and the priority actions.
The above rules and principles have been implemented by the River Basins Hydrogeological Plans : the framework in which measures are delivered or planned.

## Slide 7
Ministry of the Environment
Land and Sea
Directorate for Soil Protection
Flood hazard
is the probability of occurrence of a potentially damaging flood event.
The hazard expresses the probability that a damaging flood of a given severity occurs in a given timeframe (return period Tr). The return period is statistically defined as an inverse function of the probability, which can be consequently identified by the frequency of the flood event

## Slide 8
Ministry of the Environment
Land and Sea
Directorate for Soil Protection
When for instance we estimate that the return period of a flood event in a given area is 30-50 years, the probability of occurrence of such event is high; consequently this area can be defined a “high (flood) hazard area”.
Vice versa, the probability of a flood occurrence with an estimated return period of 300-500 years is low; consequently the area
affected can be defined a “low (flood) hazard area”.

## Slide 9
Ministry of the Environment
Land and Sea
Directorate for Soil Protection
The HAZARD MAPS therefore cover the geographical areas which have been flooded, which could be flooded with an indication of the probability, taking into account the existing flood defence structures. These areas shall be shown according to the three following scenarios:
Frequently occurring flood events (HIGH PROBABILITY, return period 30 - 50 years);
Less frequently occurring flood events (MEDIUM PROBABILITY, return period 100-200 years);
Extreme flood events (LOW PROBABILITY, return period 300-500 years).
For each scenario the degree of danger will also be provided by expressing water level, flow velocity or the combination of these and the identification of areas which could be subject to bank erosion and debris flow deposition.

## Slide 10
Ministry of the Environment
Land and Sea
Directorate for Soil Protection
THE MAPS OF FLOODING RECEPTORS
Show the receptors identified within the “flood hazard areas”, as the goods exposed to flooding, since potentially affected by that event.
The elements defining the receptors are: the value (people, properties, infrastructures, industrial activities, the environment) and the vulnerability (their ability to respond to the event). The combination of these elements are understood to be the consequences, in other words the impact that may result from the flood event on the exposed goods.

## Slide 11
Ministry of the Environment
Land and Sea
Directorate for Soil Protection
Flood risk
is the damage expected to people, properties, the environment, infrastructures, industrial activities, cultural heritage, considered as the combination of the probability of a flood event (hazard) and of the potential adverse consequences (value x vulnerability) to human health and life, the environment, the infrastructures and the economic activity associated with a flood event.

## Slide 12
Ministry of the Environment
Land and Sea
Directorate for Soil Protection
RISK MAPS
are provided, according to the following four risk classifications:
R1 – moderate risk: social, economic and environmental damages are low;
R2 – medium risk: probability of minor damages to buildings infrastructures and environment, not compromising human safety, use and economic activities;
R3 – high risk: envisaged problems to human safety; damages to buildings and infrastructures compromising their use and provoking hold-up of socio-economic activities and severe damages to the environment;
R4 – very high risk: envisaged losses of human lives and severe lesions to persons; severe damages to buildings, infrastructures and the environment and socio-economic activities destruction.

## Slide 13
Ministry of the Environment
Land and Sea
Directorate for Soil Protection

## Slide 14
Directorate for Soil Protection
Ministry of the Environment
Land and Sea
The assessment of the priority actions
The attention level and priority actions are identified on the basis of the hazard degree determining the level of risk
  PROTECTION:
A very high risk level contains also medium and high risk, hence represents the proirity objective for actions :
PREVENTION:
A high hazard level contains also medium and low hazard , hence represents the priority objective of attention to avoid not existing risk:
IN THE ASSESSMENT OF PRIORITY ACTIONS THE IMPACT OF CLIMATE CHANGE ON THE OCCURENCE OF FLOODS MUST BE ALSO CONSIDERED

## Slide 15
Directorate for Soil Protection
Ministry of the Environment
Land and Sea
  Prioritizing actions and scheduling allocation of financial available resources.
  Don’t let occur not existing flood risk .

## Slide 16
Directorate for Soil Protection
Ministry of the Environment
Land and Sea
Results achieved towards hydrogeological risk management
Italy has completed the hydrogeological land planning activity for floods, landslides and avalanches risk management.
The River Basin Hydrogeological Plans are developped by the River Basin Authorities. The RBHP rule over and integrate other sectorial plans in coordination with regional and local administrations and Civil Protection Units responsible for the Emergency Plans.

## Slide 17
Directorate for Soil Protection
The River Basin Hydrogeological Plans provided the following results:
hazard and risk maps for floods, landslides and avalanches, showing all scenarios;
provisions regarding land use in “high risk” and “high hazard”areas to prevent the increasing or occurring of risk;
priority actions for risk reduction, identified according to the risk degree: over No.10.000 for a value of more than 11 billions Euros;
budgeted expenses for all the identified and required actions: over 40 billions Euros.
On the basis of the Plans, a Map of the hydrogeological critical areas has been prepared to support the priority actions.
Ministry of the Environment
Land and Sea

## Slide 18
Directorate for Soil Protection
Ministry of the Environment
Land and Sea
The map of the hydrogeological critical areas*
Policy and legislation
Provision and monitoring of funding
Ministry of the Environment Land and Sea- Directorate for Soil Protection

## Slide 19
Directorate for Soil Protection
Ministry of the Environment
Land and Sea
Land surveying, monitoring and management are continuous actions which, time after time, must go on

## Slide 20
THANK YOU FOR YOUR ATTENTION
Ministry of the Environment Land and Sea
Directorate for Soil Protection
Via C. Colombo, 44
00147 Rome (Italy)
Tel. +39 06 57222636 Fax +39 06 57222620
Website www.minambiente.it